## Slide 1
DEPARTMENT OF ECE — DIGITAL DESIGN & COMPUTER ARCHITECTURE
Module 2: Combinational Logic & ALU Architecture
From Boolean Minimization to 32-Bit RISC-V Arithmetic Logic Units
Course Code: 26EC1202E

## Slide 2
Combinational Logic Foundations
Core principles governing memoryless compute blocks in digital systems
Zero Feedback Loop
Outputs depend strictly on present inputs. No storage elements, no memory states, and zero clock synchronization requirement.
Basic Gate Assemblies
Constructed directly from standard AND, OR, NOT, XOR, and NAND gates forming simple mathematical logic paths.
RISC-V Building Blocks
Forms the fundamental compute engine inside processors including ALUs, MUX selectors, Decoders, and Comparators.

## Slide 3
Expression Minimization with K-Maps
Visual reduction technique optimizing logic gate counts for high-speed hardware
Example: 4-Variable K-Map SOP
Minimal Sum-of-Products derivation eliminates redundant gate logic across multi-bit binary adders.
F(A,B,C,D) = Σ(0, 2, 8, 10)
Gray Code Order
Cells ordered as 00, 01, 11, 10 to guarantee adjacent cells differ by exactly 1 bit.
Power-of-2 Grouping
Group adjacent 1's in rectangular sizes of 1, 2, 4, 8, or 16 cells to simplify SOP.
Wrap-Around Rules
Edges and corners connect continuously to form maximum possible prime implicants.
Minimized Output: F = B' · D'

## Slide 4
Binary Arithmetic Core: Adders
Fundamental circuits executing binary addition in digital processor ALUs
Half Adder (HA)
Adds 2 single-bit inputs without prior carry in.
Full Adder (FA)
Adds 3 bits: Input A, Input B, and Carry-In (Cin).
Sum Output: S = A ⊕ B (XOR Gate)
Carry Output: Cout = A · B (AND Gate)
Limitation: Cannot accept carry input from lower bits.
Sum Output: S = A ⊕ B ⊕ Cin
Carry Output: Cout = (A·B) + Cin·(A ⊕ B)
Built using 2 Half Adders + 1 OR Gate.

## Slide 5
Ripple Carry Adder (RCA) Delay Analysis
Cascading full adders for N-bit operands and propagation delay constraints
Linear O(N) Propagation
Bit 0 (LSB)
FA 0 → Generates C1
Bit 1
FA 1 → Generates C2
Bit 2
FA 2 → Generates C3
Bit 3 (MSB)
FA 3 → Generates Cout
Total Propagation Delay Formula
t_delay = N × t_FA (where N is bit-width and t_FA is single FA delay)

## Slide 6
Controlled Binary Adder / Subtractor
Utilizing Two's Complement arithmetic via XOR conditional inversion
Hardware Reuse
Zero extra adders required. Single control wire toggles arithmetic operations instantly in RISC-V ALUs.
Addition Mode (SUB = 0)
XOR gates pass operand B unchanged (B ⊕ 0 = B). Initial carry Cin = 0. Circuit computes A + B.
Subtraction Mode (SUB = 1)
XOR gates invert operand B (B ⊕ 1 = B'). Initial Cin = 1 adds +1, completing 2's complement (A + B' + 1).

## Slide 7
Data Routing: Multiplexers (MUX)
Hardware data selectors routing multiple data channels into single outputs
2-to-1 MUX
1 Select Line (S0)
Routes Register vs Immediate values into RISC-V ALU input B.
4-to-1 MUX
2 Select Lines (S1, S0)
Selects final output among ADD, SUB, AND, and OR computation results.
8-to-1 MUX
3 Select Lines (S2, S1, S0)
Routes complex opcode operations across full 32-bit RISC-V instruction set.

## Slide 8
A1 | A0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Operation Decoding: Decoders
Converting binary code inputs into active-high one-hot signal lines
Truth Table: 2-to-4 Decoder
2-to-4 Binary Decoder
Translates 2 input lines into 4 unique output lines. Exactly 1 output line is HIGH for any input combination.
3-to-8 Control Unit Decoder
Decodes 3-bit RISC-V function fields (funct3) to enable specific hardware functional execution units.

## Slide 9
Digital Magnitude Comparators
Evaluating quantitative relationships between binary operands: A > B, A = B, and A < B
Equality (A = B)
(A0 ⊙ B0) · (A1 ⊙ B1)
Uses XNOR gates to evaluate matching bit pairs. High only when both operands are identical.
Greater Than (A > B)
A1·B1' + (A1⊙B1)·A0·B0'
Checks MSB first. If MSBs equal, evaluates LSBs for magnitude supremacy.
Less Than (A < B)
A1'·B1 + (A1⊙B1)·A0'·B0
Drives RISC-V SLT (Set-Less-Than) conditional branch operations in hardware.

## Slide 10
1-Bit Multi-Operation ALU Cell
Unifying logic gates, full adder, and MUX selection into a single bit-slice
Operation Map (2-Bit Control)
Bit-Slice Modular Design
Repeat this 1-bit logic cell 32 times and cascade carry signals (Cout → Cin) to build a complete 32-bit RISC-V CPU ALU.
Op = 00
Bitwise AND Operation
Op = 01
Bitwise OR Operation
Op = 10
Addition / Subtraction (Adder Block)
Op = 11
Set Less Than (SLT Comparison)

## Slide 11
Complete RISC-V Datapath Integration
Integrating the ALU into register files, control unit, and memory buses
1. Operand Fetch
Registers x0–x31 supply operands A and B directly to the ALU inputs in a single clock cycle.
2. Parallel Compute
ADD, SUB, AND, OR, and SLT sub-circuits evaluate inputs concurrently in hardware.
3. Result Selection
ALU Control decoder drives MUX selector lines, routing desired result to Write-Back bus.

## Slide 12
Module 2 Key Takeaways
Combinational logic forms the core execution layer of digital CPUs, translating raw logic gate equations into full arithmetic processors.
K-Map Minimization
Controlled Subtraction
RISC-V ALU Datapath